## Slide 1
Integrating Arduino with Academic Subjects
Section 3
Day Month Year

## Slide 2
Table of
Briefly describe the concept
01
02
03
04
Briefly describe the concept
Briefly describe the concept
Briefly describe the concept
Briefly describe the concept
05
06
07
08
Briefly describe the concept
Briefly describe the concept
Briefly describe the concept
CONTENTS

## Slide 3
Module 3.2
Cross-Disciplinary Applications

## Slide 4
Arduino is a user-friendly platform that enables students to design and build their own electronic projects. With a simple programming language and a wide range of hardware support, students can easily create complex electronic circuits. One of the most important features of Arduino is that it allows students to bring together different disciplines. In this way, students can utilize engineering design principles and perform mathematical calculations while using scientific methods to solve a problem.
Cross-disciplinary practices in STEM education help students develop a more holistic approach to real-world problems. For example, designing an automatic irrigation system uses knowledge from different disciplines such as plant physiology (biology), physical properties of water (physics), sensor technology (electronics) and programming (computer science). In this way, you learn to see knowledge as a whole rather than in parts.
Cross-Disciplinary Applications
Introduction

## Slide 5
?????
????
???
Cross-Disciplinary Applications
Using Arduino in art, music, and other subjects

## Slide 6
Project Name: Automatic Opening Door in Case of Fire with Arduino
Description: Using an Arduino board, we design a door system that opens automatically when smoke or toxic gas is detected.
Preparation & Research
Open doors can disrupt indoor temperature control, wasting energy in heated or cooled spaces. Automated systems, like motion-sensitive lights and doors, simplify daily life. During a fire, toxic gases pose serious health risks, and stampedes can occur if doors do not open automatically. Fire-safe doors that open outward are crucial for safety and efficient evacuation.
Cross-Disciplinary Applications
Project -1

## Slide 7
Project-1:
What do you need?:
                Computer with Internet connection
                Arduino UNO board
                MQ gas sensor
                Servo motor
                Buzzer (Sound Generator)
                Breadboard
                Jumper cable

## Slide 8
Project Name: Seeing the Temperature and Humidity of the Classroom with Arduino
Description: Using an Arduino board, we want to develop a system that displays the temperature and humidity in the classroom.
Preparation & Research: We will examine the air of our classroom like a laboratory and discover its hidden world by measuring values such as temperature and humidity. So why do we want to measure temperature and humidity? The mood of our classroom can affect how comfortable we feel while studying. Studying in an environment that is too hot or too cold can be challenging. Likewise, the humidity of the air is important for our health. How can we improve the temperature and humidity values in our classroom? For example, can we consider different methods such as opening windows and using air conditioning?
Cross-Disciplinary Applications
Project -2

## Slide 9
Project-2:
What do you need?:
1x Arduino (Uno, Nano, etc.)
1x Breadboard
1x DHT11 Temperature and Humidity Sensor
1x I2C 16×2 LCD Display
Jumper Cables

## Slide 10
Project-2:
Codes View:
#include <dht11.h>
#include <Wire.h>
#include <LiquidCrystal_I2C.h>
int temperature_value = 2;
dht11 DHT11_sensor;
LiquidCrystal_I2C lcd(0x27, 16, 2);
void setup() {
LCD.init();
LCD.backlight();
}
void loop() {
int chk = DHT11_sensor.read(temperature_value);
LCD.setCursor(0, 0);
LCD.print("Temperature= ");
LCD.print((double)DHT11_sensor.temperature, 2);
LCD.setCursor(0, 1);
LCD.print("Humidity Rate = ");
LCD.print((double)DHT11_sensor.humidity, 2);
delay(1000);
}

## Slide 11
Project Name: LIGHT Control with LDR using Arduino
Description: In this project, we will measure and control the light level required for healthy growth of plants in a greenhouse environment using Arduino. Using the light values measured by the light sensor, we will provide the optimum light level to the plants through LED lights. In this way, we can ensure that plants grow healthier and faster, and raise awareness about plant cultivation.
Preparation & Research: Plants require sunlight for photosynthesis, but their light needs vary. Research how and why different plants have specific light requirements.
A photoresistor, or photocell, changes resistance based on light intensity. In this application, an LDR controls 5 LEDs, indicating light levels based on the detected intensity.
Cross-Disciplinary Applications
Project -3

## Slide 12
Project-3:
What do you need?:
Arduino (you can use any model you want)
Breadboard
1 x 5mm LDR (Light Dependent Resistor)
5 x Red LED
5 x 330 Ohm Resistor (Orange-Orange-Brown)
1 x 10k Ohm Resistor (Brown-Black-Orange)
15 x Jumper Cables

## Slide 13
Project-3:
Codes View:
int LEDs[] = {
2, 3, 4, 5, 6
};
int number_of_LED = 5;
int ldr_pin = A0;
int value = 0;
void setup() {
for (int i = 0; i < number_of_LED; i++) {
pinMode(LEDs[i], OUTPUT);
}
}
void loop() {
value = analogRead(ldr_pin);
if (value > 0 && value <= 255) {
digitalWrite(LEDs [0], HIGH);
digitalWrite(LEDs [1], LOW);
digitalWrite(LEDs [2], LOW);
digitalWrite(LEDs [3], LOW);
digitalWrite(LEDs [4], LOW);
}
Else if (value > 256 && value <= 500) {
digitalWrite(LEDs[0], HIGH);
digitalWrite(LEDs[1], HIGH);
digitalWrite(LEDs[2], LOW);
digitalWrite(LEDs[3], LOW);
digitalWrite(LEDs[4], LOW);
}
Else if (value > 501 && value <= 700) {
digitalWrite(LEDs[0], HIGH);
digitalWrite(LEDs[1], HIGH);
digitalWrite(LEDs[2], HIGH);
digitalWrite(LEDs[3], LOW);
digitalWrite(LEDs[4], LOW);
}
Else if (value > 701 && value <= 900) {
digitalWrite(LEDs[0], HIGH);
digitalWrite(LEDs[1], HIGH);
digitalWrite(LEDs[2], HIGH);
digitalWrite(LEDs[3], HIGH);
digitalWrite(LEDs[4], LOW);
}
Else
digitalWrite(LEDs[0], HIGH);
digitalWrite(LEDs[1], HIGH);
digitalWrite(LEDs[2], HIGH);
digitalWrite(LEDs[3], HIGH);
digitalWrite(LEDs[4], HIGH);
delay(100);
}

## Slide 14
Project Name: Rain sensitive smart clothesline system
Description: In this sproject, we will design a system that detects rainfall using a water-resistant sensor and rotates the rope mechanism where the clothes are hung with the help of a motor to protect the clothes from rain.
Knowledge And Science: Have you ever thought of a way to prevent a water tank from overflowing or remaining empty? Do you know that we can do this with Arduino? Let's say we want to control the water level in a water tank. If the tank is too full, the sensor sends a signal and stops the water. If the tank is empty, the sensor can send another signal to refill the water. This sensor is a device that detects the presence or height of water. If the sensor touches the water, it sends a signal to the Arduino and we can perform an action using this signal, such as sounding an alarm or starting a pump. In this project, we will design an application that makes the motor turn when rain is detected and returns the hanging laundry to a safe area.
The working principle of the sensor used is as follows. If rain is detected, the output will be "LOW". If rain is not detected, the output will be "HIGH".
Cross-Disciplinary Applications
Project -4

## Slide 15
Project-4:
What do you need?:
Arduino (you can use any model you want)
Breadboard
Rain sensor
Servo Motor
15 x Jumper Cables

## Slide 16
Project-4:
Code View:
#include <Servo.h>
#define Rain_Sensor_pin A0
#define Servo_Motor_pin 9
Servo servo_motor;
int angle = 0;
int prev_rain;
int rain;
void setup() {
Serial.begin(9600);
pinMode(Rain_Sensor_pin, INPUT);
servo_motor.attach(Servo_Motor_pin);
servo_motor.write(angle);
rain = digitalRead(Rain_Sensor_pin);
}
void loop() {
prev_rain = rain;
rain = digitalRead(Rain_Sensor_pin);
if (rain == LOW && prev_rain == HIGH) {
Serial.println("Rain detected! The motor returns the clothesline to the safe area.");
servo_motor.write(90);
}
else
if (rain == HIGH && prev_rain == LOW) {
Serial.println("Rain stopped! The motor returns the clothesline to its original position.");
servo_motor.write(0);
}
}

## Slide 17
Assessment
1. You know that electric current is the result of the movement of charges moving through a conductor. What is the unit of electric current?
A) Volt (V)
B) Ohm (Ω)
C) Ampere (A)
D) Watt (W)
Correct answer: C
2. What material is the LDR (Light Dependent Resistor) used in designing a circuit with Arduino made of and what will be its resistance value when the light intensity increases?
A) Semiconductor material; resistance increases
B) Conductor material; resistance increases
C) Semiconductor material; resistance decreases
D) Conductor material; resistance decreases
Module 3.1

## Slide 18
Assessment
3. Which of the following sensors is used to measure the distance of an object?
A) DHT11
B) HC-SR04
C) LDR
D) MQ-2
Correct answer: B
4. Which of the following formulas expresses Ohm's Law used in electrical circuits?
A) V = I * R
B) V = I / R
C) I = V * R
D) R = V / I
Module 3.1

## Slide 19
Assessment
5. A circuit was designed for a project that measures the light level and turns on the LED when the light intensity falls below a certain value. What advantage does such a system provide?
A) Increases electric current
B) Saves energy
C) Protects circuit elements
D) Increases resistance level
Module 3.1

## Slide 20
Achivements
The projects and contents;
Emphasize energy saving, environmental awareness and sustainability.
Understanding electrical circuits, one of the physics subjects
Acquiring skills in developing strategies in biology by measuring air quality
Acquiring skills in activating another system (physics) by measuring air temperature (Chemistry)
Developing biological skills by calculating the role of light in the growth processes of plants
Module 3.1

## Slide 21
THANK
YOU
© 2022-2024. This work is licensed under a CC BY-NC 4.0 LEGAL CODE. Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Education and Culture Executive Agency (EACEA). Neither the European Union nor EACEA can be held responsible for them.